## Slide 1: Searching for Pulsar with the Murchison Widefield Array
Mengyao Xue
2024-07-14 SPSS, Kunming
MWA SMART pulsar survey collaboration (PI: Ramesh Bhat);
Kaichao Wu, Zihan Zhang, Xiaoning Tang, Xiaoli Zhang (Computer Network Information Center, CAS);
Qiuyang Fu (NAOC); Yukai Zhou (PKU)

## Slide 2
Perth
~200 km
Geraldton
41,000 km2 = The Netherlands
Population density = 0.002 people / km2
MRO (Murchison Radio-astronomy Observatory)
    Precursor for the SKA-low at the same site
Murchison Widefield Array (MWA)

## Slide 3
    Phase I (2012 -- 2016)
    128 tiles, distributed in ~ 3 km diameter region
      - each tile contains 16 dipoles, 4×4 dual polarisation array
    Low-frequency phased array
    Working frequency: 80-300 MHz
    Bandwidth: 30.72 MHz (24*1.28 MHz)
Murchison Widefield Array (MWA)
Tingay et al. (2013)

## Slide 4
    Phase II (2016 -- )
    256 tiles in total, but can only use 128 tiles at a time
      (because of the maximum signal throughput of the MWA hardware)
    Two type of configuration:
      compact and extended for different science goal
Murchison Widefield Array (MWA)
Wayth et al. (2018)

## Slide 5: Observing pulsars with the MWA the “voltage capture” (VCS) way
    Record all channelised voltage streams from each tile
    Bandwidth: 30.72 MHz (24 coarse channels, 1.28 MHz each)
    Time resolution: 100 μs Frequency resolution: 10 kHz
    Data rate: 28 TB per hour Maximum recording: 1.5 hour
Tremblay et al. (2015)
Voltage capture (VCS)
MWA correlator

## Slide 6
    Record all channelised voltage streams from each tile
    Bandwidth: 30.72 MHz (24 coarse channels, 1.28 MHz each)
    Time resolution: 100 μs Frequency resolution: 10 kHz
    Data rate: 28 TB per hour Maximum recording: 1.5 hour
Tremblay et al. (2015)
Voltage capture (VCS)
Observing pulsars with the MWA the “voltage capture” (VCS) way

## Slide 7
    The first pulsar was discovered at 81.5 MHz
    Majority of currently known pulsars were discovered and studied at higher frequency (e.g. 1.4 GHz) because:
          - Less ISM propagation effects
          - Less Galactic continuum emission background
          - Less earth ionosphere effects
    However, pulsar studies at low radio frequencies can
Credit: Tom hassall
Pulsar studies at low radio frequencies
    Provide insights into the emission mechanism of pulsars
      Profile evolution with frequency
      Spectral index (low frequency turn over; break; flattening)
    Provide valuable information about the interstellar medium

## Slide 8: Some low-frequency pulsar surveys
Bhat et al. (2023)

## Slide 9: Southern-sky MWA Rapid Two-metre (SMART) pulsar survey
Bhat et al. (2023)
2022: receiver update to MWAX
128 tiles → 144 tiles
Legacy data:
35 TB per observation
Notes: 文章中写错了（推测是因为用 28TB/hr*1.5hr得到的）

## Slide 10: Southern-sky MWA Rapid Two-metre (SMART) pulsar survey
70 observations in total（B:13，R: 13，G: 15，P: 14，O: 15），
Each observation is 4800s long，covers ~ 600 deg2，need 5000~8000 tied-array beam
Legacy data: 35 TB x 51 = 1.78 PB; MWAX data: 79 TB x 19 = 1.5 PB; In total: 3.28 PB
2022: receiver update to MWAX
128 tiles → 144 tiles
MWAX data:
79 TB per observation
May – August 2023
Credit: Chris Lee
Notes: 文章中写错了（推测是因为用 28TB/hr*1.5hr得到的）

## Slide 11: Coherent beamformed data: tied-array beam
Each observation is 4800s long，covers ~ 600 deg2，need 5000~8000 tied-array beam
For each tied-array beam, the full polarization data is 175 GB; therefore, 5000 beams account for 875 TB
Bhat et al. (2023)
Notes: main lobes overlap by 20%
155MHz ~23’; 140MHz ~25.3’; 170MHz ~20.7’

## Slide 12: New pulsar discoveries made by MWA-SMART survey
J0036-1033
J1002-2044
J0452-3418
Bhat et al. (2023), Grover et al. (2024)

## Slide 13: Independent pulsar discoveries by MWA-SMART survey
Also detected in GBT pulsar survey GBNCC
Parkes discovery, but mislabeled as J1358-2533
Position: 13:58:42_-25:33 → 13:57:24_25:30:39
DM: 31.27 → 16.05
Qiuyang Fu
J0026-1955
J1357-2530

## Slide 14: Known-pulsar detections
Pulsars: 217
Millisecond pulsars: 15
Binary pulsars: 15
First detections below 300 MHz: 34
Bhat et al. (2023), Lee in prep.

## Slide 15
The ‘first pass’ shallow search of the SMART survey
  Only analyzed the first 10 minutes of 80% legacy observations
  No RFI mitigation
  Coarse de-dispersion plan (2358 trials)
Next step
  A more thorough search on 4800s data (e.g. finer DM step)
  But the computing resources limitation ……

## Slide 16: Data transfer & store
Object storage
So far have transferred 47(/51) legacy observations (1.64 PB) & 3(/19) MWAX observations (0.24 PB)
Stored on cstcloud
With the help from Xiaoning Tang

## Slide 17
Yukai Zhou
Original coherent beam-forming code (CUDA)
Hip version beam-forming code
(https://github.com/fxzjshm/MWA-vcstools)

## Slide 18: De-dispersion Plan update and introduce down-sampling in time
Total DM trials = 6046
Total DM trials = 2358
Down-sampling by a factor of 4 in time

## Slide 19: MWA SMART full observation searching test at CNIC
Data set: two 4800s observations
For 144 point beamforming
  Beamforming takes 90 hr in total
  Pulsar search takes 75 hr in total
Beamforming
Shared storage
Pulsar search
Kaichao Wu, Zihan Zhang
Computing resources:
  3 nodes
  Each contains one 32-core CPU & 4 DCU cards
For one point beamforming
      (90+75) hour✖️12DCU➗144 pointings =13.75 DCU hour/pointing
Assume each observation can be covered with 6000 pointings
      13.75 DCU hour/pointing✖️6000 pointings = 82500 DCU hours
With 100 four-DCU-card nodes, processing one observation will take
      82500 DCU hours ➗ 400 DCU ➗ 24 hours = 8.6 days

## Slide 20: Some known pulsar detections from the test

## Slide 21: Future works
Data transfer:
  Aim for transfer rest of the legacy (4/51) & MWAX (16/19) data to CNIC
Beamforming and searching on a regular basis:
  With a more efficient searching pipeline
  Be more selective in choosing the beamforming positions
  Hope to make new pulsar detections