## Slide 1: Expectation of Cosmic Ray Energy Spectrum with LHAASO
L. L. Ma, S.S.Zhang, B.Y. Bi, L.Q.Yin, Z.Z. Zong for LHAASO collaboration
IHEP,CAS
Beijing China

## Slide 2: Outline
Difficulties in cosmic ray detection
LHAASO introduction
LHAASO science in cosmic ray measurement
Performance study of LHAASO detectors
Summary

## Slide 3: Difficulties in cosmic ray detection
Energy > 100 TeV Air shower measurement
  EAS array
  Cherenkov telescope or Array
  Fluorescence telescope
Calibration of primary energy estimate uncertain.
Composition measurement difficult
Model dependent

## Slide 4: LHASSO Introduction
1KM2 Array (KM2A)
5195 scintillator detectors every 15 m
1171 muon detectors every 30m
Wide Field of View Cherenkov telescope Array (WFCTA)
18 Telescopes
Energy meaurements
Hillas
Geometry reconstruction ，
Muon content
Geometry reconstruction
Core information
Water Cherenkov detector Array
(WCDA) 78,000m2
4400m above sea level

## Slide 5: Water Cherenkov Detector Array(WCDA)
Total cell: 3600
Total area: 90000m2
Time resolution: <2ns
Two types PMTs: 8 inches and 1 inch
Increase the dynamic range
Get the core information

## Slide 6: KM2 Array (KM2A)
 | ED | MD
Effective area | 1m2 | 36m2
Spacing | 15m | 30m
NO. of detectors | 5195 | 1171
Time resolution | 2ns | 10ns
1.2m
2.8m
Muon number
Core reconstruction : 5m
Direction reconstruction: 0.3°
Red:iron
Blue:proton
10PeVEnergy<100PeV

## Slide 7: Wide Field Cherenkov Telescope Array (WFCTA)
Reflectors:
  25 spherical mirrors
  Side length：300mm
  curvature：5800mm
Cameras
  32 x 32 SiPMs
  Wenston Cone
  Pixel diameter:25.4mm
  Focal length: 2870mm
Hillas Parameters
Xmax
Energy reconstruction

## Slide 8: LHAASO science in cosmic ray measurement
Measure individual cosmic ray spectra from 10TeV to EeV
  Multi-parameters, Multi-stages
  10TeV-100TeV
  Energy Scale
  WCDA, WFCTA
100TeV-10PeV
  Knees for H,He,…
  WCDA, WFCTA, KM2A
10PeV-100PeV
  knee of Fe
  WFCTA, KM2A
100PeV-2EeV
  2nd knee & composition changing
  Transition from galactic to extra-galactic
  WFCTA, KM2A

## Slide 9: Energy scale of WFCTA prototype
80m
Wide Field of View Cherenkov Telescope (WFCTA/LHAASO)
5m2 spherical mirror；
16×16 PMT array
Pixel size 1°；
FOV: 14°× 16°;
Elevation angle: 60°.
One of Cherenkov event
CREAM:
1.09x1.95x10-11(E/400TeV)-2.62
ARGO-YBJ:
1.95x10-11(E/400TeV)-2.61
LHAASO Prototype:
0.94x1.95x10-11(E/400TeV)-2.62
    The knee of (700±230stat.±70sys.) TeV is found

## Slide 10: Performance of LHAASO detectors from 100TeV to 10PeV
WCDA
  Core reconstruction: 3m
  Arrival direction reconstruction: 0.3°
  No. of particles near the core
WFCTA
  SIZE (total PE in image)
  Width, Length
  Distance between arrival directions to the image center
KM2A
  Total Muon number

## Slide 11
Shower generation
  CORSIKA 6990
  Energy range: 100TeV ~10PeV
  Compositions:
    Proton, helium, CNO, MgAlSi, iron
  hadronic model: QGSJETII02+ GHEISHA
Pointing direction of WFCTA
  28°，35°in zenith
  Xdepth: 700g/cm2

## Slide 12: Correlations of parameters

## Slide 13: Aperture and contaminations
 | Proton | Proton+helium
Aperture m2Sr | 1500 | 4000
Purity | 90% | 95%
Proton + helium

## Slide 14: Event rates and expected spectra based on 15% duty circle
ARGO-WFCTA model
Horandel model
H4A model

## Slide 15: Performance of LHAASO detectors from 10PeV to 100PeV
600m,766.2m
Carried out by KM2A, WFCTA
KM2A:
  Geometry reconstruction
  No. of Muons
  No. of electromagnetic particles
WFCTA:
  Px: angular distance between shower arrival direction and the image center
  Npe: Number of pe. in the Cherenkov image

## Slide 16
Air depth of LHAASO
Air depth with zenith 45°
Shower generation
  CORSIKA V74005
  Energy range: 10PeV ~100PeV
  Compositions:
  Proton, helium, CNO, MgAlSi, iron
  hadronic model: QGSJETII04+FLUKA
Pointing direction of WFCTA
  45°in zenith
  0~360°in azimuth

## Slide 17: Composition separation
Obtained from KM2A
Log10(Ne/Nmuon)
Blue: iron
Red:proton
Obtained from WFCTA
Distance: the angular distance between image center to the arriving directions

## Slide 18
WFCTA
KM2A
Purity in selecting iron: 84%
Purity in selecting iron and MgAlSi: 94%

## Slide 19: Energy reconstruction
The reconstructed energy is a function total Npe recorded by WFCTA and Rp
Energy resolution
  <20% (Rp<100m)
  <25%(Rp<200m)
  ~30%(Rp<300m)
Rp<100m
Rp<200m
Rp<300m

## Slide 20: Effective aperture and event rate
All particle
Iron
50m<Rp<250m
50m<Rp<230m
50m<Rp<200m
100 irons
15% duty cycle
15% duty cycle

## Slide 21: Summary
Due to the low energy threshold of LHAASO detectors, energy scales of the detectors can be obtained by crossing calibration with direct measurements
Proton or proton + helium spectra can be obtained by WCDA, KM2A, WFCTA with high statistics and high purity 90% for proton and 95% purity for proton and helium
Iron spectra can be obtained by KM2A, WFCTA with 100 gold events at 100PeV and 87% purity
With multiple detectors LHAASO can measure individual spectra of cosmic rays in a broad energy range

## Slide 22: Thanks for your attention