## Slide 1: SiPM-based Camera for the Image Air Cherenkov Telescope of LHAASO
Shoushan Zhang for LHAASO collaboration
Institute of High Energy Physics, Beijing, China
KIAA-WAP II, Aug. 17-19, 2017, Beijing

## Slide 2
PMT-based Image Air Cherenkov Telescope and Fluorescence Detector：
  Image Air Cherenkov Telescope： VERITAS，HESS，MAGIC …
  Florescence Detector：HIRES，TA，AUGER …
  Run on a moonless night
  PMT aging or damaged due to strong light exposure
  Duty cycle: ~10%
How to get a higher duty cycle?
LHAASO-WFCTA 样机PMT阵列增益随时间的演化
LHAASO-WFCTA prototype (PMT-based)
Motivation
PMT aging with time

## Slide 3: Silicon photomultiplier (SiPM)
Advantages: photon counting response, high detection efficiency, high gain at low bias voltage，no aging due to light exposure and no sensitive to magnetic fields.
SiPM can not be aging due to strong light exposure: SiPM-based camera can be operated in moon conditions, thus achieve a higher duty cycle than PMT-based camera. The duty cycle of SiPM-based camera is about 30%, while the PMT is only 10%.
Is made of an (APD + quenching resistor ) array
APD: operates in Geiger mode, the output signal is 0 and 1 analog signal
APD size: 15 μm – 100 μm
1600 APDs/mm² （25μm）

## Slide 4: Application example
The first G-APD Cherenkov telescope （FAST）： La Palma, Canary Islands, Spain，2011 (prototype)
  FOV ：4.5°，1440 pixels，mirror size: 9.5㎡，pixel size：0.11°
CTA: Single mirror small size telescope (5 TeV – 300 TeV), Schwarzschild-Couder telescope
FACT
CTA：SiPM-based camera

## Slide 5
WCDA:78,000 m2 3000 cells (25m2/cell)
WFCTA:
16 Cherenkov telescopes (1024 pixels/telescope)
LHAASO
KM2A:
5195 EDs
1171 MDs
Daochen, Sichuan (29o21’ 31” N, 100o08’15” E, 4410 m a.s.l., 600 g/cm)

## Slide 6: Wide Field of View Cherenkov Telescope (WFCTA)
SiPM camera
5m2 spherical mirror；
32×32 SiPMs array
Pixel size 0.5°；
FOV: 14°× 16°.
A prototype of WFCTA
instead of

## Slide 7: LHAASO-WFCTA vs. CTA
 | CTA-SSTs | LHAASO-WFCTA
Energy range | 5 TeV – 300 TeV | 30 TeV – 1 EeV (Cherenkov mode: 30TeV – 10 PeV, 10PeV-100PeV; Fluorescence mode: > 100PeV)
Diameter of mirror | ~ 4 m | ~ 2.3 m
Pixel size | ~ 0.25 | ~ 0.5
Number of pixels | 1296 | 1024
Dynamic range | 1 pe - 2000 pe | 10 pe – 32000 pe
Light pulse duration | 6 ns - 50 ns | 6 ns - 3 μs
Observation mode | Cherenkov light | Cherenkov and Fluorescence light
Fluorescence light spectrum
Air shower Cherenkov light spectrum

## Slide 8
 | SiPM | PMT
Dynamic range | Proportional to the total number of APD cells | Dependent on PMT type, HV distribution and readout method
Photon counting | Yes | No
Charge resolution | 12-13%@100pe，4%-5%@1000pe | 12%@100pe, 4%@1000pe
Pulse duration | 20 - 60 ns | ~6 ns
Dark count rate | ~80 kHz/mm² @ thrd=0.5 pe | <1kHz @ thrd=0.5 pe
Aging@strong light exposure | No aging | Aging
Magnetic fields | No sensitive | Sensitive
Gain | 1×106 @ several tens volts | 1×106 @ >1000 V
Gain vs. temperature | ~1.5%/℃ | ~0.2%/℃
SiPM vs. PMT

## Slide 9: Schematic diagram of SiPM camera assembly
AB1
AB2
DB
Cluster
SiPM camera box
SiPM camera：32×32 SiPMs
64 ×
A module has 4×4 SiPMs.
Optical filter

## Slide 10
Digital Board
Analog Board
Slow control
board
Metal frame
SiPM board
Winston cone
Light concentrator (Winston cone): is to increase the effective area of the SiPM
SiPM board: 16 SiPMs, 16 temperature sensors (embedded in the SiPM chip ), and 16 pre-amplifiers
Slow control board:
  16 temperature and high voltage compensation loops;
  16 channels of high voltage power supply.
Analogue board: 16 channels of amplifier and shaping circuit
Digital board: 50 MHz FADC and FPGA
  Square SiPM：15 mm×15 mm

## Slide 11
Outlet: 15 mm×15 mm
Inlet: 24.4mm×24.4mm
Height: 25.3mm
  Square SiPM：15 mm×15mm
Pixel size: 25.4 mm × 25.4 mm
SiPM size: 15 mm × 15 mm
light concentrators

## Slide 12
4 × 4 SiPMs & Preamplifiers
Service
TCP/IP
Switch
Low voltage power supply
Slow Control Board
64 ×
DB
FPGA
50M 14 bit FADC
50M 14 bit FADC
BDB
Trigger & Data Buffer & Communication Board
Event trigger
Data
AB
Low
gain
High
gain
Synchronizing
TCP/IP
The SiPM gain (break down voltage) is sensitive to the temperature.
Slow Control Board: temperature & high voltage compensation loop.
16 ×
Temperature
High
voltage
The architecture
of SiPM camera
readout electronics
Single trigger

## Slide 13
R3
-
+
vcc
SiPM
C1
R0
R1
OPA 846
R2
Pre-amplifier
A prototype of SiPM board
A prototype of AB
and DB board
Low light intensity response
0pe
1pe
2pe
3pe

## Slide 14
  HAMAMASTU SiPM
Ncell =230,400
The dynamic range of the SiPM is proportional to the total number of cells.
  Larger area SiPM has a bigger DCR.
  The small APD size: will produce small fill factor and then small PDE.
  SiPM with photosensitive area=15mm×15mm and APD size=25μm is selected.
The deviation <1% @ 32000 pes, if the SiPM gain is overestimated or underestimated by 10%.

## Slide 15
Light spot from the reflective mirror
Estimate the non-linearity from the non-uniform light distribution cause by the light spot and the light concentrators
Light distribution output from the cone
~1.5% @ 32000 pes

## Slide 16
PMT
FBK
Charge resolution:
  SiPM: ~5%@1000pe
  PMT: ~4%@1000pe
  HAMAMASTU
SensL

## Slide 17: I-V curve for breakdown voltage and quenching resistor
Linear fit
Breakdown voltage: 53.3 mv/℃
Gain: ~1.5%/℃

## Slide 18: Gian monitor
Mirror
UV light 400 nm
SiPM camera
UV LED
UV-LEDs are mounted at the center of the mirror to monitor and calibrate the gain of the SiPM-based camera.
  The SiPM gain (break down voltage) is sensitive to the temperature.
  The voltage drop on the R0 (VR0 ) varies with the intensity of the sky background light. Accordingly, the supply voltage or the gain of the SiPM varies with the intensity of the sky background light.
  To monitor the high gain and the low gain of the electronics.
UV-LEDs configutation
  The photons intensity: ~3000 photons/pixel.
  Pulse width <20 ns and frequency of 1 Hz
  Monitoring accuracy: <1% per minute.
R3
-
+
vcc
SiPM
C1
R0
R1
OPA 846
R2
The supply voltage of the SiPM is equal to Vcc-VR0 .

## Slide 19
The relative deviation is less than 2% with C1=1 μF.
The long light pulse response
Light pulse duration
  Cherenkov light: 6ns – 50 ns
  Fluorescence light: tens of ns - 3us

## Slide 20
Sky background light spectrum
in the moon less night

## Slide 21
Chart: 
Chart: 
Filter window：AR + cutoff

## Slide 22
 | FBK | SensL | Hamamatsu | PMT （R7899）
Relative PDE/QE | 38%@400 nm | 31%@400 nm | 29%@400 nm | 16%@400 nm
Dark count rate | 18 MHz | 11.3MHz | 11.3MHz | <1kHz
Sky background noise | ~49 MHz | ~40 MHz | ~32 MHz | ~24MHz
Signal to noise ratio
SiPM: 15mm×15mm，25μm

## Slide 23: Trigger algorithm
First level trigger：single channel trigger
Signal to noise ratio: S/N>n
Threshold varies with the intensity of the sky background light.
Second level trigger： pattern recognition
Round-shaped
pattern
Line-shaped pattern
One of Cherenkov event
Fluorescence event
Site2
Site1
Site3
Energy threshold of the telescope: ~30 TeV @ moonless night, ~300 TeV @ half moon night.

## Slide 24: Summary
SiPM camera are designed and can meet the requirements of LHAASO-WFCTA
  SiPM-based camera can be operated on moon nights and achieve a longer duty cycle than PMT-based camera. The duty cycle of SiPM-based camera is about 30%, while the PMT is only 10%.
    -- Energy threshold of the telescope: ~30 TeV @ moonless night, ~300 TeV @ half moon night.
    -- SiPM based camera and PMT based camera almost have the same S/N at a moonless night.
Time schedule
  First SiPM camera will be built before Jan. 2018;
  6 telescopes based on SiPM camera will be built and run before the end of 2018.
  16 telescopes will be run at 2020.

## Slide 25: Thank you for your attention!

## Slide 27
Moon trajectory
North
East
South
West
Cherenkov telescope array: 16 telescopes are aimed from north-east to north-west.

## Slide 28: SiPM candidates: HAMAMATSU, SensL and FBK
 | FBK (25 μm) | SensL (25 μm) | Hamamatsu （25 μm）
PDE | 38%@400 nm | 31%@400 nm | 29%@400 nm
Fill factor | 72% | 62% | 47%
Dark count rate | ~80kHz/mm2 | ~50k/mm2 | ~45k/mm2
Optical cross talk | ~15% | ~5% | ~1%
Gain | ~2×106 | ~0.9×106 | ~0.7×106
Break down voltage | ~26.5V | ~24.5 | ~53V
Gain vs. temperature | ~1.5%/℃ | ~1.5%/℃ | ~1.5%/℃
Break down voltage vs. temperature | ~26 mv/℃ | ~24 mv/℃ | ~54 mv/℃

## Slide 29
荧光事例
荧光观测模式布局