## Slide 1: A wide Field of View atmospheric Cherenkov telescope based on a refractive water-lens for future gamma-ray astronomy
Tianlu Chen, Qi Gao, … (Tibet University)
Yi Zhang, Cheng Liu, Hui Cai, Zhen Wang, Hongbo Hu, … (IHEP)
BEIJING, CHINA, 2017/08/19

## Slide 2
Outline
Introduction
Concept of Water-Lens Telescope
First Observation of CRs with the Prototype
Statues and Future Plans
Discussion and Conclusion
High altitude candidate site in Tibet

## Slide 3
Motivation
A wide field of view and large dimensional Atmospheric Cherenkov Telescope array at high altitude site for observation of sporadic γ-ray sources, i.e, VHE emission of GRBs, possible VHE electromagnetic counterparts of
Gravitational Waves, VHE emission of AGNs.

## Slide 4
Why Study GRBs at Very High Energy (GeV-subTeV) ?
Acceleration mechanisms , energetics, and therefore constrain the progenitors and jet feeding mechanism
Understanding progenitor then leads to an understanding of cosmology & stellar evolution required to support progenitor population
Extragalactic background light induced absorption (EBL absorption) of high energy photons
Limits on Lorentz Invariance Violation
Potential ultra high energy cosmic ray sources
Gamma-ray bursts: the most violent explosions in the universe

## Slide 5
GRB Name | Photon Emax | Redshift
GRB080916C | 13GeV | 4.35
GRB090510 | 31GeV | 0.903
GRB090902B | 33GeV | 1.822
GRB090926A | 19.6GeV | 2.1
GRB130427A | 95GeV | 0.145
GRB 940217 | 18GeV | /
GRBs have energies up to at least 100GeV.
VHE emission of GRBs in Fermi era
LAT: 30 MeV–300GeV
GRB 130427A
Science, 2014, 343(6166), p.42(6) ; p.38(4) ; p.51(4);p.48（4）
APJS, 2016, 223:28 (18pp), 2016
Notes: In gamma ray astronomy, Gamma ray bursts is long-lasting excited area. The are flashes of gamma rays associated with extremely energetic explosions that have been observed in distant galaxies.
A few of GRBs have very high energy photons, up to tens of GeV, even near to100GeV.Here list some fomous GRBs with very high energy photos.
Observation of GRBs with energy at sub-100GeV is meaningful.

## Slide 6
Status of VHE γ-ray
S.Z. Chen, SCIENTIA SINICA Physica, Mechanica & Astronomica, 45,119503, 2015
Sensitivities of VHE gamma ray detectors. The three curves of Fermi indicate the sensitivity of 4 years observation for different positions (l=0◦, b=0◦), (l=0◦, b=30◦), (l=0◦, b=90◦) . The performance for HESS, MAGIC, VERITAS, CTA is based on 50 hours of data taking; for Tibet ASγ (ASγ+MD presented here is for final layout that include 12 MDs and a full filled array), Milagro, ARGO-YBJ, HAWC, LHAASO, it is based on one year of data.
To detect very high energy emission of sporadic γ-ray sources by future ground-based γ-ray experiment, larger FoV and lower energy threshold are the two most important goals to achieve.
The low sensitivity at sub-100 GeV is the weakness of the current γ-ray detecting techniques.
Notes: 图 19 (网络版彩图) 各实验灵敏度, 其中 Fermi 从上至下三
条线分别代表 (l=0◦, b=0◦), (l=0◦, b=30◦), (l=0◦, b=90◦) 位
置处 4 年观测时间,为50 h观测时间(MAGIC为最新的双镜联合观测);
Tibet ASγ(ASγ+MD为12个MD水池和地面阵列全加密
结果), Milagro[34], ARGO-YBJ[32],, HAWC[34], LHAASO[35]
为一年观测时间

## Slide 7
Novel technique using lenses: a lens can work as an efficient light collector!
large FoV;
large effective area;
good transmittance;
no shadows.
Lens
(Refractive)
Camera
Camera
Mirror
(Reflective)
Wide FoV Cherenkov Telescope
Refractive Optics
Luisa Arruda, Report of PASC Winter School, Sesimbra, 12/2008
Traditional
New

## Slide 8
  A 5m2 spherical mirror
  FOV of 14o×16o with 0.5o pixels;
  to measure the energy spectrum and the composition of cosmic rays (CR) in the energy range from 30 TeV to several EeV.
S. S. Zhang, et.al , NIMA 629 (2011) 57–65
S. S. Zhang KIAA-WAP II Session 5: Gamma-ray II
Wide FoV Cherenkov Telescope
Reflective Optics
Schmidt-type IACT
R. Mirzoyan et.al APP 31 (2009) 1–5
Meridian Atmospheric CHErenkov TElescope (MACHETE)
J. Cortina et.al., APP 72 (2016) 46–54
Each of the two telescopes would have a camera with a FOV of 5×60 sq deg oriented along the meridian. About half of the sky drifts through this FOV in a year.
A spherical shape of 34 m radius .
Optical PSF of 0.06°for an ideal mirror.
15,000 photodetectors.
WFCTA/CRTNT
Mirror: 45m×14m=620m2
Camera: 1.5m×18m=27m2
Notes:   Although there is some wide field view Cherenkov telescope array, such as WFCTA, the aim is to measure the energy spectrum and the composition of cosmic rays (CRs),not to devoted to gamma ray astronomy .The detail of WFCTA will see Zhang Shoushang’s talk tomorrow

## Slide 9: GAW: Gamma Air Watch
T. Fujii, et.al APP 74 (2016) 64–72
Wide FoV Cherenkov Telescope
Refractive Optics
Large dimensional Fresnel lens is very expensive.
G. Cusumano ICRC2011:ID1352
JEM-EUSO is a Fresnel-optics refractive telescope devoted to
the observation of Ultra High Energy Cosmic Rays (UHECR).
Casolino M et al., (JEM-EUSO Collaboration) 2014 Exp. Atron.
Lens diameter 2650mm
Field of View(FoV) ±30o
1.5m diameter three lens optics
The prototype lens also used by FAST have detected some candidates UHECRs in time coincidence with the TA FD.
The optics of GAW, composed by a large dimensional single-sided Fresnel lens, will allow to achieve large field of view.

## Slide 10
Conceptual design for the water-lens telescope array
Our concept is inspired by the structure of human eye.
High transmittance of purified water for ultraviolet photons
A refractive water-lens telescope with acrylic shell as a light collector for observing Cherenkov light induced by CRs and high energy γ-ray, especially aiming for detecting the high energy emission of sporadic γ-ray sources.
Large dimensional water-lens is relatively cheap.
Effective
aperture
Purified
waters
n=1.33
0° 20°
Aperture
The focal plane and camera
Light concentrator
Glass shell
n=1.49
Lens
n=1.41
Vitreous humor
n=1.34
Human eye

## Slide 11
Aperture：6.9m
Effective aperture:5m
Focal length： 12m
Point spread function (PSF) r80: 80mm (0.38o)
Field of View： 40o×40o
Array: 4 Telescopes
Preliminary simulation result: Effective Area
 | CTA(LSTs) | Water-lens telescope
Dimension | 24m | 5m（effective aperture）
Telescope number | 4 | 4
Effective area(m2)@60GeV | ~104m2 | ~103m2
Field of View | tens of square degrees | thousand of square degrees

## Slide 12
Water-lens prototype
As a pathfinder, we designed and manufactured a water lens prototype with a thin spherical cap. We have successfully observed Cherenkov light induced by high energy CRs in coincidence with a scintillator EAS array in Yangbajing Observatory.
Ø=0.9m

## Slide 13
λ=420nm
r80≤30mm
Between the incident angle of 0o and 15o, the transmittance is approximately uniform around 89%.
The FOV of 14o×14o and 27o×27o will have 68% and 50% encircled energy respectively
For the focal length of 168 cm, r80 =30mm corresponds to ~1o, i.e, the focal plate scale of 2.9 cm deg-1.
The optical property of water-lens prototype
The surface accuracy of lens is ±1mm which has been assessed by industrial Computerized Tomography (CT).

## Slide 14
Layout of the coincidence expeiment
Water-lens
Experiment conducted at Yangbajing Observatory in November 2016
Off-line coincidence with the scintillator EAS array
scintillator detector array
Camera
R7725 PMT: 51mm (1.74o)
center hexagonal (37pixels) +outer guard ring (12 pixels)
The full aperture of the camera is 15o ×13o.

## Slide 15
First observation of CRs
Water-lens
  Events:1.79×107
  N1=157.7Hz.
EAS array:
  Events:2.95×106
  N2=26.04Hz
Coincident event
  Coincident time window 400ns.
  Events:5.18×104
  N=0.46Hz.
Accidental coincident rate
  R=2N1N2τ=0.003Hz.
Therefore the accidental coincident rate can be ignored, which indicates that the coincident events are real Cherenkov light induced by CRs.

## Slide 16
Typical CRs events
The intersection angle between the reconstructed direction of the EAS array and the water-lens is 0.5o.
EAS Array

## Slide 17
∆α (Sigma) =1.36±0.13o
∆β (Sigma) =1.34±0.12o
The angular resolution of the EAS array can be estimated from Monte Carlo simulation, which is ~0.9o .
In this case, the angular distribution of the water-lens telescope is estimated as ~0.9o, which is consistent with the expectation.
Estimation of angular distribution
Coincident events :
∆α, ∆β denote the E-W and N-S differences between the reconstructed direction cosine of the EAS array and one of water-lens.
No 21 PMT

## Slide 18
Statues and Future Plans
Step1
0.9m lens + EAS Array
CRs (done)
Step2
2m lens (being manufactured)
Step3
5m（Effective aperture） (2×2) lens
VHE emission of sporadic γ ray sources (e.g, GRBs)
Crab

## Slide 19: High altitude (>5000m) candidate site in Tibetan Plateau
L. W. Jones and D.M. Mei, ICRC1999, 2.524.
Higher altitude can lower the energy threshold and enhance the effective area.
Notes: Next step we plan enlarge the dimension of water lens. Besides, we also could put the water-lens array at higher altitude to achieve lower energy threshold.
In fact, as early as 1999, Prof Jones proposed to built cosmic ray station above 6000-m elevation.
This is the ICRC article of Prof. Jones.

## Slide 20
Pumajiangtang elementary school:5030m
Kangnila Pass:5200m
Ali-CPT I site： 5260m
Xiaozidaban, Ali, 6000m
5300m
2017.07
High altitude (>5000m) candidate site in Tibetan Plateau
2017.08
2016.07
Notes: We also investigated some candidate sites in Tibetan plateau.
Locating at an altitude above 5000M altitude and accessible by high class road, the PuMaJiangTang has been identified as a suitable site for EAS experiment. There are tens of kilometers large area flat land, convenient traffic (215KM to LHASA), sufficient power (Tibet Middle Part Power Grid is covering this area), convenient communication (The base stations of China Mobile and China Telecom are in service, mobile can be sued)
phone can be used normally.), suitable for survival (~1000 local residents).
This candidate site reported by a CMB observation group.

## Slide 21
  IACT that based on refractive optics may provide a innovative way for the ground-based γ ray astronomy by achieving a very large FoV.
The prototype telescope has successfully observed Cherenkov light that has induced by CRs .
The prototype telescope can achieve a 15o×13o FoV and a ~0.9o angular distribution which is suitable for taking certain Cherenkov images for air showers.
A larger dimensional water-lens with wide FoV at high altitude site would be used to lower the energy threshold for γ ray astronomy, especially for detecting VHE emission of GRBs, AGNs, and possible VHE electromagnetic counterparts of Gravitational Waves.
Discussion and conclusion

## Slide 22
The end
Thank you!

## Slide 23
Coincidence with EAS array (Matching with Time Clock)
  FADC give every trigger signal a Trigger Time Tag, it records the Trigger arrival time; Resolution is ~17ns (8.5ns/bin*2bin=17ns).
  The trigger signal of water lens also send to EAS array through ED electronics.
  The ED electronics give trigger signal a GPS time ( Resolution is ~1ns)
  Water lens telescope and EAS array operated independently.
  We matching the data through GPS time and Trigger Time Tag.

## Slide 24
Image of HID (Xenon)
Floodlights
Image of car headlight
The Focal Length (FL) and light spot
  fexp=168±1.5 cm, and it is basically agreed with simulation result (fsim=164 cm) using ZEMAX.
3.2cm
Notes:   We measured the focal length at outdoor, the distance between the light source and the lens was about 400 meters, it is very far and we can regard the light as approximate parallel light, so we obtain focal lens fexp=168±1.5 cm, and it is basically agreed with simulation result (fsim=164 cm) using ZEMAX.
The first figure shows a photo with coordinate paper of the optimal image of HID (Xenon) Floodlights
the focus spot is Dexpspot=32 mm, and it is consistent to simulation
results Dsimspot=30 mm (see Figure 3(b)) by using the real FL fexp=168 cm in simulation.
The second Figure shows a photo of the optimal image of car headlight (distance between two lamps
is 1.5 m, we can see obvious superposition of two image.

## Slide 25
r80 equals to 80mm, which corresponds to 0.38 degree for the focal length f=12m.
~10000 PMT 40o×40o

## Slide 28
The influence of muon event on observation
  Coincidence measurement method
  When scintillator tiggers (trigger rates:~280Hz ), records 9 PMT signals
  Test1:PMTs with shade cover
  Test2:PMTs without shade cover
  Test results:
    Test 1: coincidence rate ~0.71 Hz;
    Test 2: coincidence rate ~0.63 Hz (muon hits on PMT directly);
  Discussion: To this prototype, muon event have little influence on observation.